## Slide 1
CSE499A · FINAL PRESENTATION
Neural
Rover
A Wi-Fi-controlled mobile robot with live pan–tilt video and fail-safe motion control
Jubayed Ahmed Sahel · Fahad Hossain Shourov
Pujon Chakraborty · Anonna Rahman Spondon
North South University · Supervisor: Dr. K. M. A. Salam
Notes: Presenter: Jubayed Ahmed Sahel | Target time: 0:30
Introduce the team and the central result: the CSE499A rover platform is complete; face recognition remains the next-stage module.
Use the rover photograph to identify the completed physical platform, then move directly to the problem the system solves.
[Sources]
- IEEE_499A_Report/Neural_Rover_IEEE_499A_Report_Final.pdf
- Project Files/Neural Rover Home Veranda.png (user-supplied project image)

## Slide 2
WHY NEURAL ROVER
Remote inspection needs control and awareness
A mobile platform is useful only when the operator can move it, see its surroundings, and stop it safely from one place.
MOVE
Four-wheel directional control from a phone or laptop
SEE
Live camera stream embedded in the same browser interface
AIM
Independent pan, tilt, and illumination control
STOP
Local fail-safe response when communication disappears
LEAD PRESENTER · Jubayed Ahmed Sahel
02
Notes: Presenter: Jubayed Ahmed Sahel | Target time: 0:55
Frame the engineering problem as control plus visual awareness plus safety—not simply an RC car.
Use the four verbs as the project acceptance logic.
[Sources]
- README.md
- IEEE_499A_Report/Neural_Rover_IEEE_499A_Report_Final.pdf

## Slide 3
SYSTEM ARCHITECTURE
How every module connects across the rover
Main ESP32 controls motion and safety; ESP32-CAM streams video; one power system connects both.
LEAD PRESENTER · Jubayed Ahmed Sahel
03
BROWSER / PHONE
Drive commands Live video Camera aim
MAIN ESP32
Web server + WebSocket PWM / direction Watchdog + fail-safe
ESP32-CAM
Camera capture MJPEG stream Flash LED
2 × L298N
Left + right channels Four motor outputs
PAN / TILT
Two SG90 servos GPIO 13 + GPIO 4
4 DC MOTORS
Front + rear Left + right drive
CAMERA AIM
Pan 0–180° Tilt 0–180°
OPERATOR
PROCESSING
ACTUATION
ROVER RESPONSE
Wi-Fi · WebSocket
MJPEG
UART2
PWM + DIR
GPIO PWM
POWER + GROUND 3S battery → L298N motor rail | LM2596 → regulated 5 V for both ESP32 boards + servos | all modules share common ground
Notes: Presenter: Jubayed Ahmed Sahel | Target time: 1:30
Start at the browser: control commands travel over Wi-Fi and WebSocket to the main ESP32.
The main ESP32 owns motion, pan/tilt, the watchdog, and the fail-safe stop. It sends PWM and direction to the two L298N drivers, which run all four motors.
The ESP32-CAM handles capture and MJPEG streaming. UART2 keeps the two boards coordinated without letting video load block the motor safety loop.
Finish with power: the 3S battery feeds the motor rail; the LM2596 provides regulated 5 V; every module shares common ground.
[Sources]
- README.md
- Project Files/Neural Rover Architecture Detailed.png

## Slide 4
HARDWARE IMPLEMENTATION
Accessible modules form a complete rover
01
CONTROL
30-pin ESP32
Web server · PWM · UART2
02
VISION
ESP32-CAM
MJPEG stream · flash LED
03
MOTION
2 × L298N
4 geared DC motors
04
VIEW + POWER
2 × SG90 servos
3S battery · LM2596 at 5.0 V
LEAD PRESENTER · Fahad Hossain Shourov
04
Notes: Presenter: Fahad Hossain Shourov | Target time: 0:55
Name the four physical layers; avoid reading component lists verbatim.
Explain that two motor drivers give four independent reversible channels and the LM2596 isolates the regulated logic rail.
[Sources]
- README.md
- RC_CAR_COMPLETE_INFORMATION.md

## Slide 5
ELECTRICAL DESIGN
Shared power design makes integration reliable
MOTOR RAIL
3S battery → both L298N motor inputs
LOGIC RAIL
LM2596 → regulated 5.0 V for both ESP32 boards and servos
SIGNAL REFERENCE
Battery, controllers, drivers, and servos share one common ground
LEAD PRESENTER · Fahad Hossain Shourov
05
Notes: Presenter: Fahad Hossain Shourov | Target time: 1:05
Explain why USB success alone did not prove vehicle stability: motor startup current and switching noise affect the logic rail.
Call out regulated 5 V, common ground, and the UART crossing between boards.
Handoff: Pujon will cover the control experience and safety firmware.
[Sources]
- RC_CAR_COMPLETE_INFORMATION.md
- Project Files/ESP32-CAM-Connection with hardware.jpeg

## Slide 6
OPERATOR EXPERIENCE
One browser page unifies control and video
Persistent WebSocket control keeps commands responsive while MJPEG video remains visible in the same interface.
DRIVE
Press-and-hold F / B / L / R · Stop on release
WATCH
Live stream from ESP32-CAM on port 81
AIM
Pan P0–P180 · Tilt T0–T180 · Flash control
CONTROL LOOP
Browser
↓ WebSocket commands
Main ESP32
↓ PWM + direction
Four motors + pan / tilt
LEAD PRESENTER · Pujon Chakraborty
06
Notes: Presenter: Pujon Chakraborty | Target time: 1:00
Demonstrate the control logic verbally: hold to move, release to stop, and keepalive while held.
Mention the browser integrates the camera rather than requiring separate control and video pages.
[Sources]
- README.md
- RC_CAR_COMPLETE_INFORMATION.md

## Slide 7
FAIL-SAFE CONTROL
Safety is enforced on the rover—not in the browser
Any lost control path returns every motor enable output to zero.
01
Button release
02
Stale command
03
Browser disconnect
04
Wi-Fi loss
40
ms reversal
dead time
1300
ms command
timeout
Direction reversal first neutralizes PWM and motor polarity, then applies the new command.
LEAD PRESENTER · Pujon Chakraborty
07
Notes: Presenter: Pujon Chakraborty | Target time: 1:10
Make the safety claim explicit: the browser is only a client; the rover owns the stop decision.
Use the two numeric anchors to explain dead time and stale-command timeout.
Handoff: Anonna will summarize validation and the next phase.
[Sources]
- README.md
- IEEE_499A_Report/Neural_Rover_IEEE_499A_Report_Final.pdf

## Slide 8
PROJECT STATUS
499A is complete; face recognition comes next
COMPLETED AND VERIFIED
✓ Four-wheel motion and corrected motor polarity
✓ Browser + WebSocket control with reconnection
✓ Live ESP32-CAM stream in the control page
✓ Pan, tilt, and camera-light control
✓ Power integration, UART discovery, and fail-safe stop
✓ System testing, documentation, and IEEE report
NEXT-STAGE MODULE
Face
recognition
Laptop-side InsightFace processing will consume the rover’s existing MJPEG stream.
LEAD PRESENTER · Anonna Rahman Spondon
08
Notes: Presenter: Anonna Rahman Spondon | Target time: 1:00
State the boundary confidently and honestly: all embedded rover objectives are complete; face recognition is not presented as finished.
Point out that the completed stream and network architecture already provide the input required by the AI module.
[Sources]
- README.md
- RC_CAR_COMPLETE_INFORMATION.md
- IEEE_499A_Report/Neural_Rover_IEEE_499A_Report_Final.pdf

## Slide 9
NEXT PHASE
499B adds an independent AI layer
01
INGEST
Read the existing MJPEG stream on the GPU laptop
02
RECOGNIZE
Enroll known people and compare face embeddings
03
RESPOND
Log events; later add fall detection and caregiver alerts
Key advantage: the AI layer can evolve independently because motion safety remains on the main ESP32.
LEAD PRESENTER · Anonna Rahman Spondon
09
Notes: Presenter: Anonna Rahman Spondon | Target time: 1:00
Explain the three-step roadmap: stream ingestion, face enrollment/recognition, then event response.
Treat fall detection and alerts as later extensions, not completed deliverables.
[Sources]
- NEURAL_ROVER.md
- Next plans.txt
- RC_CAR_COMPLETE_INFORMATION.md

## Slide 10
NEURAL ROVER
A complete rover platform—
ready for its AI layer.
Demo path
Connect → Drive → Stream → Pan / Tilt → Fail-safe stop
Questions?
CSE499A · North South University
LEAD PRESENTER · Anonna Rahman Spondon
10
Notes: Presenter: Anonna Rahman Spondon | Target time: 0:30 + questions
Close by resolving the opening: Neural Rover now combines motion, visual awareness, and local safety in one tested platform.
If a live demo follows, use the sequence shown. Invite questions after the fail-safe stop demonstration.
[Sources]
- README.md
- IEEE_499A_Report/Neural_Rover_IEEE_499A_Report_Final.pdf